## Slide 1
BROWNBAG SERIES / SESSION 2
Clear requirements make
disagreement visible.
Writing clear, atomic flight-software requirements
45-60 minutes | no preparation | discussion-driven
ONE SENTENCE
periodically
DEV
every cycle
TEST
once/min
OPS
on event
Flight Software Requirements Writing & Review
01
Notes: PURPOSE
Open Session 2 and establish that clarity is about controlling technical interpretation, not polishing prose.
SUGGESTED SCRIPT
Welcome back. In Session 1 we treated a requirement as an engineering agreement. Today we focus on making that agreement clear and atomic. A vague word such as periodically can produce several reasonable interpretations: every control cycle, once per minute, or only after an event. The sentence may sound understandable while the engineering obligation remains undefined. Our goal is to make disagreement visible early, while it is still cheap to resolve.
FACILITATION CUE
Ask the room what periodically means to them before pointing to the three interpretations. Accept several answers; the variation is the point.
TRANSITION
Here is how we will move from that ambiguity to a practical writing and review habit.

## Slide 2
SESSION MAP
The hour moves from interpretation to atomic behavior.
SESSION 2
02
0-5
RECAP
Why, What, Evidence
5-15
OWN
Choose the correct subject
15-25
CLARIFY
Obligation words and vague terms
25-35
ATOMIZE
One primary obligation
35-55
PRACTICE
Review and rewrite together
55-60
CLOSE
Five checks before review
Protect the practice time: that is where the writing habits become usable.
Notes: PURPOSE
Set expectations for the Session 2 sequence and reserve most of the hour for collaborative review and rewriting.
SUGGESTED SCRIPT
We will begin with a short recap of the three questions from Session 1. Then we will focus on choosing the right subject, using obligation words consistently, replacing vague terms with measurable behavior, and deciding when one sentence contains too many obligations. We will spend the final third of the session reviewing and rewriting battery-state examples together. Everything happens here; there is no homework.
FACILITATION CUE
For a 45-minute session, shorten the recap and modal-verb discussion. Preserve slides 11 through 15.
TRANSITION
Let us reconnect today's writing techniques to the review model from Session 1.

## Slide 3
WEEK 1 RECAP
Clear and atomic strengthens the What without losing Why or Evidence.
SESSION 2
03
WHY
Why is this behavior necessary?
WHAT
Exactly what must happen?
EVIDENCE
How will we objectively verify it?
TODAY'S FOCUS
One defensible interpretation. One primary obligation.
Notes: PURPOSE
Connect Session 2 to the Week 1 model and show that clarity and atomicity improve the definition of the required behavior.
SUGGESTED SCRIPT
Our Week 1 questions still apply: Why, What, and Evidence. Today we are zooming in on the What. Clear means the words support one technically defensible interpretation in the relevant context. Atomic means the requirement contains one primary obligation that can be traced, changed, and verified coherently. We still need the Why to validate necessity and the Evidence to confirm the result.
FACILITATION CUE
Ask someone to name the three Week 1 questions without reading the slide. Keep the recap brief and friendly.
TRANSITION
First, we need a useful definition of clarity.

## Slide 4
CLARITY
Clear means one technically defensible interpretation.
SESSION 2
04
SOURCE STATEMENT
The Flight Software shall periodically validate ephemeris data.
DEVELOPER
Validate every execution cycle
TESTER
Validate at a fixed time interval
OPERATOR
Validate when new data arrives
If multiple interpretations are reasonable, the requirement is carrying an unresolved decision.
Notes: PURPOSE
Define clarity in engineering terms by showing how an apparently simple sentence creates multiple reasonable implementations and tests.
SUGGESTED SCRIPT
This statement is grammatically simple, but periodically has no defined engineering meaning. A developer may check every cycle. A tester may choose an interval. An operator may expect validation only when new data arrives. None of those interpretations is absurd. That is the warning sign. If multiple interpretations are technically reasonable, the requirement is carrying an unresolved decision. Clarity is not about using short words; it is about controlling interpretation in context.
FACILITATION CUE
Ask the room for a fourth interpretation. Then ask what information would collapse the possibilities: trigger, frequency, applicable mode, or interface event.
TRANSITION
Clarity begins with naming the element that actually owns the behavior.

## Slide 5
OWNERSHIP
Put the shall on the element that owns the action.
SESSION 2
05
TOO BROAD
The spacecraft shall reject an invalid command.
SPACECRAFT
System behavior
FLIGHT SOFTWARE
Software allocation
COMMAND INGEST
Owning software element
The Command Ingest application shall reject a command with an invalid opcode.
Notes: PURPOSE
Teach writers to assign the obligation to the software element with authority and responsibility for the action.
SUGGESTED SCRIPT
The spacecraft is often too broad a subject for a software requirement. Which element evaluates the command? Which element has authority to reject it? Naming the owning software element improves allocation, traceability, interface review, and testing. The right level depends on the architecture and the specification level. Do not force a low-level component name into a higher-level requirement, but do not hide ownership behind the word system when ownership matters.
FACILITATION CUE
Ask whether reject means discard, refuse execution, send a negative acknowledgment, or all three. This reveals that choosing the subject does not by itself finish the behavior definition.
TRANSITION
Once the subject is correct, the sentence still needs to distinguish obligations from facts, goals, and permissions.

## Slide 6
OBLIGATION WORDS
Shall marks an obligation; it cannot rescue weak behavior.
SESSION 2
06
SHALL
Binding requirement
The application shall reject an invalid opcode.
WILL
Declaration or fact
The ground system will provide time correlation data.
SHOULD
Recommendation or goal
The display should minimize operator workload.
MAY
Permission or allowed option
The operator may retry a rejected command.
Follow your organization's convention. Consistency supports review and verification.
Notes: PURPOSE
Clarify the usual roles of shall, will, should, and may while emphasizing that modal consistency does not substitute for technical precision.
SUGGESTED SCRIPT
Many engineering organizations use shall for a binding requirement, will for a declaration or fact, should for a recommendation or goal, and may for permission. Follow the convention in your governing process. The important point is consistency. Also notice that shall only marks a sentence as an obligation. It does not make the subject correct, the behavior measurable, or the requirement atomic. The sentence shall respond appropriately is still weak.
FACILITATION CUE
If your organization uses different definitions, state them here and edit the slide later. Avoid turning this into a standards debate; the next slides address the harder technical issues.
TRANSITION
The most common clarity defects come from ordinary words that hide engineering decisions.

## Slide 7
VAGUE TERMS
Replace vague adjectives and adverbs with engineering decisions.
SESSION 2
07
VAGUE WORD
DECISION IT HIDES
quickly
response time or deadline
periodically
frequency, interval, or trigger
as needed
explicit condition or authority
nominal
allowed state, range, or data quality
appropriate / adequate
observable response and pass/fail limit
Do not replace vague words with invented numbers. Resolve the source decision.
Notes: PURPOSE
Give reviewers a practical translation from common vague words to the specific engineering decisions they conceal.
SUGGESTED SCRIPT
These words are not forbidden because they sound informal. They are risky because they hide different decisions. Quickly hides a deadline. Periodically hides an interval or trigger. As needed hides a condition or authority. Nominal hides an allowed state or range. Appropriate and adequate hide the observable response and acceptance limit. The fix is not to invent a number during wordsmithing. The fix is to identify the authoritative source and resolve the technical decision.
FACILITATION CUE
Ask the team for one vague term they see often. Translate it into the question a reviewer should ask. Keep project-specific criticism anonymous.
TRANSITION
Clarity controls interpretation. Atomicity controls how many obligations the sentence asks us to manage at once.

## Slide 8
ATOMICITY
One primary obligation supports one coherent pass/fail decision.
SESSION 2
08
COMPOUND
The Power Management application shall detect low battery state, set a warning, and command Low-Power Mode.
DETECT
Determine that the low-battery condition is present
REPORT
Set the low-battery warning telemetry
RESPOND
Issue the Low-Power Mode transition request
Split when obligations need independent conditions, timing, traceability, change, or verification.
Notes: PURPOSE
Explain atomicity as an engineering management property, not a rule that every requirement must be extremely short.
SUGGESTED SCRIPT
This sentence contains detection, reporting, and response obligations. Those actions may have different conditions, timing, owners, parent traces, verification methods, and change histories. If two actions pass and one fails, the sentence does not support a clean pass/fail decision. Atomicity means one primary obligation with a coherent verification result. It does not mean we split every noun or field into a separate requirement.
FACILITATION CUE
Ask which of the three actions might change independently during design or operations. That often makes the value of splitting more concrete than grammar rules do.
TRANSITION
Conjunctions help us find possible compounds, but they are review signals rather than automatic defects.

## Slide 9
REVIEW SIGNAL
And and or are clues, not automatic defects.
SESSION 2
09
ONE OBJECT
The application shall include the time tag and validity flag in each sample record.
One action; two required fields
TWO ACTIONS
The application shall detect stale data and command Low-Power Mode.
Independent behavior and evidence
LOGIC
When voltage is low or current is high, the application shall set the power warning.
Is or inclusive? Are thresholds defined?
Ask: Can each action or condition change and pass independently?
Notes: PURPOSE
Give reviewers a nuanced way to use conjunctions as prompts for inspection without banning ordinary grammar.
SUGGESTED SCRIPT
Scanning for and and or is useful, but neither word automatically makes a requirement defective. The first example has one action, include, applied to a record with two required fields. The second has two actions with independent evidence and probably should be split. The third may contain acceptable condition logic, but the meaning of or and the thresholds must be explicit. The review question is whether parts can change, fail, or be verified independently.
FACILITATION CUE
Ask the room to classify each example before explaining it. Emphasize that context and the verification concept decide whether a split helps.
TRANSITION
We can now combine ownership, clarity, and atomicity in one writing structure.

## Slide 10
WRITING STRUCTURE
Expose the condition, owner, primary action, and measurable bound.
SESSION 2
10
CONDITION
When three consecutive valid battery samples are at or below 25 percent,
OWNER
the Power Management application
PRIMARY ACTION
shall issue a Low-Power Mode transition request
BOUND
within 2 seconds.
Primary verb: issue. One obligation. The threshold, sample quality, count, and deadline are explicit.
Notes: PURPOSE
Provide a reusable sentence pattern that combines the Session 2 concepts into one technically inspectable requirement.
SUGGESTED SCRIPT
This example exposes the condition, owning software element, primary action, and measurable deadline. The condition defines valid samples, threshold, and persistence count. The owner is allocated. The primary verb is issue, so the obligation is not confused with mode-transition completion. The two-second bound makes the response verifiable. This structure is a guide, not a rigid template. Keep the elements that the behavior requires and make omissions intentional.
FACILITATION CUE
Ask which clock starts the two-second deadline and whether issue means place on an interface, receive acknowledgment, or complete the transition. Those questions prepare the team for the practice slides.
TRANSITION
Let us apply the model to a sentence with several hidden decisions.

## Slide 11
REVIEW PRACTICE 1
Vague words are unanswered design and verification questions.
SESSION 2
11
During normal operations, the Flight Software shall periodically check battery state and take appropriate action.
NORMAL
Which modes or states?
PERIODICALLY
At what interval or trigger?
BATTERY STATE
Which data, validity, units, and range?
APPROPRIATE
What observable response?
DISCUSS
Choose the first technical decision you would resolve before attempting a rewrite.
Notes: PURPOSE
Practice turning vague words into specific review questions and discourage superficial rewrites that invent missing technical intent.
SUGGESTED SCRIPT
This sentence hides several decisions. Normal operations needs mode or state scope. Periodically needs a frequency or trigger. Battery state needs a defined source, validity rule, units, and range. Appropriate action needs an observable response. We should not immediately replace periodically with a convenient number. First identify which source owns the decision: operations concept, interface specification, hazard control, or parent requirement.
FACILITATION CUE
Give the team one minute to identify defects. Then ask which decision must be resolved first and why. Favor answers that establish data meaning and triggering conditions before wording.
TRANSITION
The next example is more specific, but it carries several independent obligations.

## Slide 12
REVIEW PRACTICE 2
Specific words can still conceal a compound requirement.
SESSION 2
12
When battery state of charge is low, the Flight Software shall set a warning, shed payload loads, and enter Survival Mode.
Set warning
Telemetry state and deadline
Shed payload loads
Authority, interface, and sequence
Enter Survival Mode
Request or confirmed transition?
Each action may have a different owner, condition, sequence, and pass/fail result.
DISCUSS
Which actions belong to this software element, and which need separate requirements?
Notes: PURPOSE
Practice identifying independent obligations and questioning whether the named software element has authority for every action.
SUGGESTED SCRIPT
The wording is more concrete than the previous example, but it contains at least three obligations. Setting a warning, shedding loads, and entering a mode can have different owners, interfaces, timing, and verification methods. The phrase state of charge is low is also undefined. Before splitting the sentence, validate allocation: perhaps Power Management requests load shedding while another application executes it, and perhaps software requests Survival Mode rather than entering it directly.
FACILITATION CUE
Ask one group member to act as developer and another as tester. Have each describe the minimum information they need. Capture differences in ownership and pass/fail evidence.
TRANSITION
Now we will write from a small set of agreed facts instead of guessing at missing intent.

## Slide 13
GROUP REWRITE
Write one atomic obligation from agreed technical facts.
SESSION 2
13
MODE
Applies in Normal Mode
DATA
Valid battery state-of-charge samples arrive at 1 Hz
TRIGGER
Three consecutive samples at or below 25 percent
OWNER
Power Management application
ACTION
Issue a Low-Power Mode transition request
DEADLINE
Within 2 seconds of the third qualifying sample
Write the requirement. Then review it for subject, one primary action, defined condition, and measurable bound.
DISCUSS
Take 3 minutes. Build one sentence, then let another person review it.
Notes: PURPOSE
Provide a constrained in-session writing exercise where the technical intent is supplied, allowing the team to focus on clarity and atomicity.
SUGGESTED SCRIPT
For this exercise, the technical facts are already agreed. Write one requirement that preserves all six facts. Use the correct owner, one primary action, an explicit condition, and a measurable deadline. After the first sentence is proposed, someone else should review it. The reviewer should not rewrite immediately; first identify any alternate interpretation or missing pass/fail detail.
FACILITATION CUE
Allow about three minutes. Capture the exact wording. Useful review questions include whether at or below is preserved, whether the third sample starts the clock, and whether issue means request generation or confirmed receipt.
TRANSITION
Here is one defensible version and the questions it still does not answer.

## Slide 14
DEBRIEF
A clear requirement can expose the next decisions without inventing them.
SESSION 2
14
POSSIBLE REQUIREMENT
While operating in Normal Mode, when three consecutive valid battery state-of-charge samples are at or below 25 percent, the Power Management application shall issue a Low-Power Mode transition request within 2 seconds of receiving the third qualifying sample.
WHAT IS RESOLVED
Mode, data validity, threshold, and persistence
Owning element and one primary action
Clock start and response deadline
WHAT REMAINS OUT OF SCOPE OR TBD
Hysteresis and recovery behavior
Missing or invalid sample behavior
Request acknowledgment and failed transition
Notes: PURPOSE
Debrief the exercise with a defensible answer while showing that clarity should reveal unresolved scope rather than silently invent it.
SUGGESTED SCRIPT
This version preserves the supplied facts. It names the applicable mode, valid data, threshold, persistence rule, owner, primary action, clock start, and deadline. It also reveals what the exercise did not define: hysteresis and recovery, missing or invalid samples, acknowledgment, and failed transition behavior. Those may require other requirements or explicit decisions. A strong requirement narrows interpretation without pretending to answer questions outside its approved intent.
FACILITATION CUE
Compare this wording with the team's version. Treat differences as review material, not a grading exercise. Ask whether any remaining item belongs in this requirement or in a separate atomic requirement.
TRANSITION
We will close with five checks that fit on the edge of a real review.

## Slide 15
CLOSE
Before sending a requirement to review, run five checks.
SESSION 2
15
01
OWNER
Is the subject the element that owns the action?
02
OBLIGATION
Is there one primary action and a consistent shall?
03
MEANING
Are conditions, terms, units, and ranges defined?
04
BOUND
Is the behavior measurable where a limit matters?
05
EVIDENCE
Can verification produce one coherent pass/fail result?
Clear enough to share one interpretation. Atomic enough to share one decision.
Notes: PURPOSE
Close with a short pre-review checklist that participants can apply without a formal worksheet.
SUGGESTED SCRIPT
Before sending a requirement to review, check five things. Is the subject the element that owns the action? Is there one primary obligation? Are conditions, terms, units, and ranges defined? Is the behavior measurable where a limit matters? Can verification produce one coherent pass/fail result? These checks do not replace the full review checklist. They remove avoidable ambiguity before review time is spent.
FACILITATION CUE
Ask each participant to choose the check they will consciously use in their next review. End without assigning homework; the commitment is optional and immediate.
TRANSITION
Thank the team. Session 3 will focus on making requirements verifiable through measurable behavior and appropriate verification methods.

## Slide 16
FACILITATOR APPENDIX
Protect practice time and ask for interpretations before corrections.
APPENDIX
16
0-5 min
OPEN
Use periodically to surface multiple reasonable interpretations.
5-15 min
OWN
Recap Week 1, then discuss subject and authority.
15-25 min
CLARIFY
Cover modal conventions briefly; spend time translating vague terms.
25-35 min
ATOMIZE
Use conjunctions as review signals and introduce the sentence structure.
35-55 min
PRACTICE
Prioritize slides 11-14; let participants review one another's wording.
55-60 min
CLOSE
End with the five checks. No homework.
Facilitator stance: ask what decision the word hides before proposing replacement wording.
Notes: PURPOSE
Provide an optional facilitator-only reference for timing, discussion management, and the 45-minute fallback.
SUGGESTED SCRIPT
This slide is for preparation rather than normal presentation. Protect the practice section. The most useful facilitation move is to ask what technical decision a vague word hides before anyone proposes replacement text. Encourage participants to state alternate interpretations and verification consequences. Keep examples impersonal and treat disagreement as evidence that the requirement needs more context.
FACILITATION CUE
Hide this slide before presenting if desired. For 45 minutes, compress slides 3, 6, and 9; retain slides 10 through 15.
TRANSITION
End of facilitator appendix.